## Slide 1
SMART INDIA HACKATHON 2026
Problem Statement ID – SIH26162
Problem Statement Title- AI-Based Detection and Classification of Industrial Fires and Persistent Thermal Sources Using NASA FIRMS, OSM & Satellite Data
Theme- Disaster Management
PS Category- Software
Team ID-
Team Name (Registered on portal) - Fire Orbit
Organisation: National Technical Research Organisation (NTRO)

## Slide 2
THERMALSENTINEL — CORE SOLUTION OVERVIEW
NASA FIRMS shows where the ground is hot; ThermalSentinel says what is burning and whether it is abnormal — classifying every thermal anomaly and alerting only on real industrial incidents.
[OUR SOLUTION]
[HOW IT WORKS & ARCHITECTURE]
[UNIQUE DIFFERENTIATORS]
NASA FIRMS reports thousands of hot pixels over India every day — a refinery flare, a steel plant, a coal-seam fire, a stubble burn and a forest fire look identical.
ThermalSentinel classifies every detection into 6 classes with a confidence and plain-language reasons.
It tracks each thermal SOURCE for 90 days and builds a persistent-source registry.
It alerts only when a known site burns far above its own baseline — a real incident, not routine heat.
Output is a GIS map layer + GeoJSON API: the PS asks for segregation of industrial fires and GIS storage/visualisation; both are live today.
INGEST: FIRMS VIIRS 375 m + MODIS (NRT ≤ 3 h + archive), both sensors normalised, passes de-duplicated
CLUSTER: Haversine DBSCAN 750 m groups pixel-jittered detections into thermal sources (22 k → 4.4 k)
PERSISTENCE: 90-day history per source: active days, span, night %, FRP mean / CV / z-score
CONTEXT: OpenStreetMap facility type + distance and land cover (STRtree point-in-polygon)
CLASSIFY: Explainable rules + gradient-boosted trees on 34 features; FRP-anomaly detector
SERVE: SQLite → FastAPI GeoJSON → React/Leaflet GIS dashboard; QGIS / ArcGIS export
✦ Source-level persistence fingerprint
classify the source over 90 days, not a single pixel
✦ Baseline-relative incident alerts
FRP ≥ 2.5× the site's own normal & z ≥ 3 → 0.6 % of data
✦ OSM infrastructure + land-cover fusion
facility type, distance and land use as model features
✦ Explainable hybrid AI
every label carries human-readable reasons — auditable
[OPERATIONAL PROCESS FLOW & PROTOTYPE WORKFLOW]
[STEP 1: DATA CAPTURE]
FIRMS API pulled in 10-day chunks; 22,179 detections in the 90-day archive
[STEP 2: SOURCE CONTEXT]
DBSCAN clusters + OSM facilities & land cover around hotspot cells
[STEP 3: ANALYSIS & AI]
34 features → rules + GBM vote → class, confidence, reasons
[STEP 4: ACTIONABLE OUTPUT]
138 incident candidates (0.6 %) on the GIS map with FRP evidence
[STEP 5: VALIDATION]
Sentinel-2 SWIR / Worldview verification; analyst override retrains

## Slide 3
FIRE ORBIT
TECHNICAL APPROACH
3
[INPUT] NASA FIRMS
VIIRS 375 m · MODIS 1 km
[DATA INGESTION]
Area API · 10-day chunks
Normalise VIIRS + MODIS
de-duplicate passes
CONTEXT LAYERS
OSM facilities (Overpass)
Land-cover polygons
Sentinel-2 / Worldview links
Cluster
Persist
Score
[CORE PROCESSING]
DBSCAN 750 m → thermal sources
90-day stats: active days, span,
night %, FRP μ / CV / z-score
→ persistence score
[FEATURE MATRIX]
34 features: radiometry · persistence ·
OSM context · land cover · season priors
[VALIDATION]
group-aware split · analyst override → retrain
[STAGE 2A] RULE ENGINE
persistent ∧ night ≥60 % ∧ steady FRP
→ GAS FLARE (auditable priors)
[STAGE 2B] GBM MODEL
HistGradientBoosting · 6 classes
probability ≥ 0.55 wins
[STAGE 3: AI / ML OUTPUT]
class · confidence · reasons
industrial · flare · mining ·
agri · wildfire · other
⚠ ANOMALY ALERT
FRP ≥ 2.5 μ and z ≥ 3
→ incident candidate
[STAGE 5] GIS SERVE
GeoJSON API · dashboard · QGIS
[TECH STACK TAG]
[DATA INGESTION & GEOSPATIAL]
• NASA FIRMS Area API (VIIRS/MODIS)
• OpenStreetMap Overpass · shapely STRtree
[BACKEND & DATABASE]
• Python 3 · FastAPI (GeoJSON REST)
• SQLite → PostGIS-ready schema
[FRONTEND & GIS INTERFACE]
• React 18 + Vite · Leaflet canvas (40 k+ pts)
• QGIS / ArcGIS export · GitHub Pages demo
[INTELLIGENCE & MODELING]
• scikit-learn: DBSCAN, HistGradientBoosting
• Rule engine + FRP-anomaly detector
🗄️
[Dataset Metric]
22,179 detections
classified in ~7 s
🕒
[Temporal Metric]
90-day window
rolling baseline per source
📍
[Spatial Metric]
750 m / 1.5 km
cluster radius · facility match
📋
[Review Metric]
138 alerts
analyst verification step

## Slide 4
FIRE ORBIT
FEASIBILITY AND VIABILITY
4
[TECHNICAL FEASIBILITY]
✓ NASA FIRMS (free MAP_KEY)
✓ OSM / Overpass context
✓ Sentinel-2 & NASA Worldview
✓ Software-only · one VM
✓ Incremental 10-day ingest
[OPERATIONAL VIABILITY]
✓ Disaster-management fit
✓ Analyst confirm / override
✓ Alert prioritisation (0.6 %)
✓ GIS investigation workflow
✓ Human-in-the-loop verification
[CHALLENGES & MITIGATION]
Thermal ≠ fire → persistence + context
Persistent heat → own-baseline alerts
Cloud / data gaps → 90-day, 3 satellites
Few ML labels → rules prior + feedback
[SCALABILITY & COST]
Open data — ₹0 licences
Software-first, Docker-ready
Incremental processing
Multi-region / national potential
Modular, PostGIS-ready
22,179
DETECTIONS
90 DAYS
BASELINE
1.5 KM
OSM CONTEXT
HUMAN-LOOP
VERIFICATION
Prototype runs today: whole 90-day archive classified in ~7 s on a laptop · public demo on GitHub Pages · one env variable switches to live NASA FIRMS.
[FEASIBILITY & VIABILITY TAG]
[Feasibility key points]
• All data free & open; no procurement
• End-to-end prototype already working
[Viability key points]
• ₹0 data cost; ~₹3–5 k/month single VM
• GeoJSON plugs into NTRO / Bhuvan GIS
[Risk & Challenges]
• Simulated archive is cleaner than reality
• OSM gaps; clouds; false alarms
[Mitigation & Future Work]
• Validate on documented incidents; retrain
• Sentinel-2 chip CNN; ESA WorldCover
🗄️
[Critical Risk Highlight]
Thermal ≠ fire
persistence + OSM context resolve it
⚙️
[Operational Viability]
~7 s / 90 days
seconds of compute per national run
📈
[Scalability Factor]
India-wide
around-cell OSM queries + cache
💰
[Cost Optimization]
₹0 data
open sources; one VM deployment

## Slide 5
FIRE ORBIT
IMPACT AND BENEFITS
5
WHO BENEFITS
BEFORE → THERMALSENTINEL
🏭
Industrial safety & plant operators
🚨
NDMA / SDMA · fire services
🛰️
NTRO & geospatial analysts
🏛️
CPCB / MoEFCC · state boards
🌱
Environment & climate reporting
Thermal points
→
Classified context
Manual screening
→
Ranked priority
Limited context
→
OSM + imagery evidence
Unclear priority
→
Baseline-relative risk
Observation only
→
Verifiable record
KEY IMPACTS
🛡️
SAFETY
99 % fewer hotspots to triage — 138 of 22,179 reach an operator
🌱
ENVIRONMENT
Stubble burning separated from industrial emissions & flaring
🚨
RESPONSE
Abnormal industrial heat flagged with facility name and FRP evidence
⚙️
OPS
Explainable labels; analyst override feeds back into the model
EVIDENCE | 22,179 detections classified in ~7 s · 114 persistent sources · 138 incident candidates · hybrid 99.9 % vs rules-only 98.4 %
live GIS prototype: https://rahulskandagal.github.io/thermal-sentinel/
THERMALSENTINEL VALUE CHAIN
DETECT → CLUSTER → CONTEXTUALIZE → CLASSIFY → BASELINE → ALERT → VERIFY

## Slide 6
RESEARCH FOUNDATIONS & ACADEMIC REFERENCES
Core Academic Studies & Validated Data — ThermalSentinel (SIH26162)
01
FOUNDATIONAL ACADEMIC RESEARCH
●
Schroeder, W. et al. (2014) | The New VIIRS 375 m active fire detection data product — Remote Sensing of Environment 143, 85–96 doi.org/10.1016/j.rse.2013.12.008
●
Elvidge, C. D. et al. (2013) | VIIRS Nightfire: satellite pyrometry at night — Remote Sensing 5(9) — basis for gas-flare signatures doi.org/10.3390/rs5094423
●
Ester, M. et al. (1996) | DBSCAN density-based clustering (KDD-96) — source grouping method scikit-learn.org
02
APPLIED STUDIES & METHODOLOGIES
●
Liu, Y. et al. (2018) | Identifying industrial heat sources from VIIRS Nightfire time-series — Remote Sensing of Environment 204 sciencedirect.com
●
ICAR-IARI CREAMS / CPCB | Crop-residue burning bulletins — Oct–Nov & Apr–May seasonality used as a classifier prior creams.iari.res.in
●
NTRO PS SIH26162 | Segregate industrial fires from forest & natural fires; GIS storage and map-overlay visualisation sih.gov.in
03
DATA SOURCES & APIs
NASA FIRMS Area API
VIIRS 375 m (S-NPP / NOAA-20 / 21) + MODIS 1 km · NRT ≤ 3 h and archive
firms.modaps.eosdis.nasa.gov
OpenStreetMap Overpass
industrial=* · man_made=flare|works · power=plant · landuse=quarry|farmland|forest
wiki.openstreetmap.org
Copernicus Sentinel-2 / Worldview
SWIR B11/B12 chips for visual verification; ESA WorldCover 10 m land cover
dataspace.copernicus.eu
CORE PROJECT RESEARCH INSIGHT
State-of-the-art systems detect raw thermal anomalies — FIRMS publishes the pixel, not its meaning. ThermalSentinel adds the interpretation layer: it groups pixels into sources, learns each source's normal, fuses OSM infrastructure and land cover, and raises an alert only when a known industrial site burns abnormally.
Validated on a labelled 90-day archive: 22,179 detections · 114 persistent sources · 138 incident candidates · hybrid 99.9 % vs rules-only 98.4 % (group-aware split).
OBSERVE
CONTEXTUALIZE
CLASSIFY
BASELINE
PRIORITIZE
VERIFY
Working prototype: https://rahulskandagal.github.io/thermal-sentinel/ Source: https://github.com/rahulskandagal/thermal-sentinel