## Slide 1
ThermalSentinel
SMART INDIA HACKATHON 2026 · SIH26162 · NTRO
AI-based detection and classification of industrial fires and persistent thermal sources
NASA FIRMS × OpenStreetMap × Satellite imagery → a GIS system that tells you what is burning, and whether it should be.
Team: <TEAM NAME> Members: <NAMES> Institute: <COLLEGE>
Notes: Opening (20 s): "Good morning. NASA already tells the world where the ground is hot — thousands of times a day over India. Nobody tells you WHAT is hot. We built the system that does." Then introduce the team in one line each.

## Slide 2
THE PROBLEM
Every hotspot looks identical from space
ThermalSentinel · SIH26162 · NTRO
2
FIRMS hotspot
lat/lon · FRP 18 MW · 08:06 UTC
Refinery flare
Jamnagar
FIRMS hotspot
lat/lon · FRP 18 MW · 08:06 UTC
Steel plant
Bhilai
FIRMS hotspot
lat/lon · FRP 18 MW · 08:06 UTC
Coal-seam fire
Jharia
FIRMS hotspot
lat/lon · FRP 18 MW · 08:06 UTC
Stubble burning
Sangrur
FIRMS hotspot
lat/lon · FRP 18 MW · 08:06 UTC
Forest fire
Uttarakhand
NASA FIRMS publishes every VIIRS / MODIS thermal anomaly within ~3 hours — location, brightness, FRP, day/night. It does NOT say what caused it.
India gets thousands of detections a day: routine factory heat, flares and coal fires sit in the same list as wildfires, crop burning and real industrial accidents.
Result: disaster managers cannot prioritise; a genuine refinery or steel-plant fire hides among thousands of "normal" hotspots.
Notes: Key message: the data exists, the interpretation does not. FIRMS is a list of hot pixels. Point to the five cards: same pixel, five completely different situations — only one of them needs a fire brigade.

## Slide 3
CONTEXT
Why this matters for India
ThermalSentinel · SIH26162 · NTRO
3
375 m
VIIRS pixel — enough to see a single furnace, flare stack or field
4+ / day
satellite passes over India (Suomi-NPP, NOAA-20/21, day + night)
100+ yrs
Jharia coal-seam fires burning — a permanent "hotspot" that is not an emergency
30,000+
farm-fire detections in Punjab alone in a single Kharif season
What NTRO asked for (PS SIH26162)
Classification & segregation of industrial fires from forest fires and other natural fires
A GIS-based solution: data storage + visualisation of the output as an overlay over maps
Integrate thermal anomaly data, land cover, industrial infrastructure databases and satellite imagery
Who is hurt today
Fire services & SDMAs respond late or to the wrong hotspots
Security agencies have no registry of persistent thermal sources or undeclared industrial activity
Pollution boards cannot separate stubble burning from industrial emissions in the same district
Notes: Tie the numbers to the story: satellites are good enough (375 m), frequent enough (4+ passes/day), but the signal is drowned — Jharia alone produces detections every single day, Punjab produces tens of thousands each season. Then read the PS requirements — we cover all three bullets.

## Slide 4
OUR SOLUTION
ThermalSentinel — what it does
ThermalSentinel · SIH26162 · NTRO
4
1
Classify
Every FIRMS detection → one of 6 classes: industrial fire / process heat, gas flare, mining & coal-seam fire, agricultural burn, wildfire, other. With a confidence and a plain-English reason.
2
Track
Groups detections into thermal sources and follows them over 90 days: active days, night fraction, FRP baseline → a persistence score and a registry of persistent sources.
3
Alert
Flags FRP anomalies: a known source burning ≥ 2.5× its own normal is an incident candidate — a real industrial fire, not routine heat.
Working prototype — interactive GIS dashboard, REST/GeoJSON API, runs on a laptop
Only free, open data: NASA FIRMS · OpenStreetMap (Overpass) · Copernicus Sentinel-2 · NASA Worldview. No licences, no cost, works offline on an archive and live with one API key.
Notes: Three verbs: classify, track, alert. Stress that "alert" is the disaster-management payoff — separating a refinery operating normally from a refinery on fire. Mention that everything on the right is running code, not a mock-up.

## Slide 5
LIVE PROTOTYPE
The GIS dashboard
ThermalSentinel · SIH26162 · NTRO
5
A
KPIs & daily timeline
detections, persistent sources, incident candidates; stacked bars per class per day
B
Top persistent sources
ranked by persistence score, one click flies to the site
C
Class filters & layers
class, date range, min confidence, persistent-only, anomalies-only
D
Map overlays
coloured detections (size = FRP), dashed footprints = persistent sources, OSM factory icons
E
Detail drawer
reasons, persistence stats, source time-series, links to Sentinel-2 / Worldview
F
GIS export
GeoJSON → QGIS / ArcGIS; full REST API at /docs
A
B
C
D
Notes: If the live demo works, switch to the browser here. Script: (1) zoom to Jamnagar — orange persistent footprint, 86 active days, the April incident spike in the timeline; (2) toggle "anomalies only"; (3) click a green dot in Punjab — cropland + season + low FRP reasons; (4) export GeoJSON. Fallback: this slide.

## Slide 6
ARCHITECTURE
How it works — the pipeline
ThermalSentinel · SIH26162 · NTRO
6
1
Ingest
FIRMS Area API — VIIRS SNPP / NOAA-20 / 21 + MODIS. 10-day chunks, NRT + archive CSV. Normalise both sensors to one schema, de-dup overlapping passes.
2
Cluster
Haversine DBSCAN (750 m). Pixel jitter between passes collapses into one "thermal source" — 22 k dots → 4.4 k sources.
3
Persistence
Per source over 90 d: active days, span, max gap, night fraction, FRP mean / CV / z-score → persistence score.
4
OSM context
Overpass queried only around hotspot cells: refineries, steel, power, flares, kilns, mines + land-use polygons (point-in-polygon).
5
Classify
Explainable rule engine + gradient-boosted trees vote. Confidence, reasons, FRP-anomaly flag.
6
Serve
SQLite → FastAPI GeoJSON API → React + Leaflet dashboard, QGIS export, imagery deep-links.
Notes: Walk left-to-right, top-to-bottom. The two clever engineering decisions to call out: (a) DBSCAN clustering — without it, persistence cannot be computed because the satellite never puts the same factory on the same pixel twice; (b) Overpass "around hotspot cells" — makes OSM context feasible India-wide instead of downloading the whole country.

## Slide 7
THE INTELLIGENCE
Three clues separate the classes
ThermalSentinel · SIH26162 · NTRO
7
Persistence (time)
Has this exact spot been hot again and again?
Refinery
86 d
Gas flare
84 d
Coal fire
86 d
Wildfire
5 d
Crop burn
1 d
active days in 90
Context (place)
What is on the ground here, per OpenStreetMap?
≤1.5 km from refinery / steel / power
man_made=flare, oil & gas field
landuse=quarry, mine
landuse=farmland (+ Apr–May / Oct–Nov)
landuse=forest, natural=scrub
Signature (physics)
How does it burn?
Steady FRP, ~50 % night, daily
Small, very steady, 80 %+ night
Low FRP, diffuse, day & night
Huge, variable FRP, spreads
Low FRP, daytime, gone next day
Notes: This is the slide that shows we understand the domain. No single clue works alone: a brick kiln on farmland, a forest fire next to a mine. The classifier sees all three at once — 34 features.

## Slide 8
THE MODEL
Hybrid classifier: explainable rules + ML
ThermalSentinel · SIH26162 · NTRO
8
Rule engine (transparent)
IF persistent ∧ night ≥ 60 % ∧ FRP-CV ≤ 0.9 ∧ near oil/gas → GAS_FLARE
IF dist(refinery|steel|power) ≤ 1.5 km → INDUSTRIAL_FIRE
IF cropland ∧ Apr–May|Oct–Nov ∧ day ∧ FRP < 25 ∧ ≤ 2 days → AGRI_BURN
IF forest|scrub ∧ not persistent ∧ > 3 km from industry → WILDFIRE
Every decision returns human-readable reasons → shown in the UI, auditable by analysts.
Gradient-boosted trees (learned)
scikit-learn HistGradientBoosting on 34 features (radiometry, persistence, OSM context, land cover, calendar)
Trained on 16,772 labelled detections, tested on 5,407 — group-aware split: all detections of one source stay on one side, so nothing leaks
ML label used when probability ≥ 0.55, else rules; agreement raises confidence
⚠ FRP-anomaly detector — the disaster-management trigger
For a persistent source with baseline FRP μ and σ: anomaly ⇔ FRP ≥ 2.5 μ and (FRP − μ)/σ ≥ 3
Found 138 incident candidates in the 90-day archive — e.g. Bhilai Steel 414 MW vs 32 MW baseline, Jamnagar 207 MW vs 19 MW. Routine operation is silent; only the abnormal day raises an alert.
Notes: Anticipated question: "why not a CNN on satellite images?" Answer: FIRMS gives us a point + FRP, not an image; the discriminating information is temporal and contextual, which tabular ML handles well and explainably. Imagery is the verification step (deep links), and a Sentinel-2 chip classifier is on the roadmap.

## Slide 9
EVALUATION
Results on the labelled 90-day archive
ThermalSentinel · SIH26162 · NTRO
9
99.9 %
hybrid ML + rules accuracy
98.4 %
rules-only accuracy
22,179
detections classified in ~7 s
114
persistent sources registered
Per-class F1 (held-out sources)
Chart: 
| Agricultural burn | Gas flare | Industrial fire / process heat | Mining / coal-seam fire | Wildfire
F1 | 99.8 | 100 | 100 | 100 | 99.3
What drives the decision (permutation importance)
Chart: 
| land cover: cropland | land cover: industrial | night fraction | near mine/quarry | near gas flare | land cover unknown | distance to industry | source mean FRP
importance | 6.95 | 2.5 | 1.61 | 1.16 | 1.02 | 0.71 | 0.59 | 0.5
Note: archive is physically-simulated over real sites, so it is clean; real-world accuracy will be lower. "Other" class had no held-out sources. Split = 16,772 / 5,407 detections.
Notes: Be upfront: the archive is synthetic-but-physical (real coordinates, realistic behaviour, labelled). The point of this slide is that the pipeline is measurable and the model learns sensible things — land cover, night fraction, proximity to infrastructure, persistence. With a FIRMS key we run on live data; with analyst-labelled incidents we retrain.

## Slide 10
OUTPUT
What the system found in 90 days
ThermalSentinel · SIH26162 · NTRO
10
Persistent source | Class | Days | Mean FRP | Night | ⚠
Paradip Refinery | Industrial fire / process heat | 90 | 11.6 MW | 66 % | 5
Jamnagar Refinery Complex | Industrial fire / process heat | 86 | 19.4 MW | 59 % | 6
Mangala Oil Field, Barmer (flare) | Gas flare | 84 | 6.0 MW | 82 % | –
Visakhapatnam Steel Plant | Industrial fire / process heat | 84 | 22.0 MW | 50 % | 4
Jharia Coalfield (coal-seam fires) | Mining / coal-seam fire | 86 | 5.8 MW | 49 % | 10
Bellary sponge-iron units | Industrial fire / process heat | 79 | 10.1 MW | 34 % | 4
Mehsana ONGC Field (flare) | Gas flare | 89 | 5.9 MW | 87 % | –
Mangala Oil Field, Barmer (flare) | Gas flare | 79 | 6.0 MW | 84 % | –
Top persistent sources by persistence score (Mar–May 2025 archive).
Note how the flares show 82–87 % night detections and a steady ~6 MW — exactly the signature the classifier keys on.
⚠ Incident candidates
FRP spikes far above the source's own baseline
Jharia Coalfield
24 MW peak vs 6 MW normal · 10 days
Tata Steel Jamshedpur
101 MW peak vs 26 MW normal · 7 days
Bokaro Steel Plant
99 MW peak vs 25 MW normal · 7 days
Jamnagar Refinery Complex
207 MW peak vs 19 MW normal · 6 days
JSW Vijayanagar Steel
115 MW peak vs 30 MW normal · 6 days
Bhilai Steel Plant
414 MW peak vs 32 MW normal · 6 days
138 of 22,179 detections flagged (0.6 %) — the short list a control room actually needs to look at.
Notes: Read the incident column: 138 flagged out of 22,179 — that is a 99.4 % noise reduction for an operator. The Bhilai example: 414 MW against a 32 MW baseline, on one day, at a known steel plant. That is the alert you want at 3 a.m.

## Slide 11
ENGINEERING
System architecture & technology
ThermalSentinel · SIH26162 · NTRO
11
Data sources
NASA FIRMS Area API (VIIRS 375 m, MODIS 1 km)
OpenStreetMap via Overpass
Copernicus Sentinel-2 / NASA Worldview (verification)
Processing (Python)
pandas · numpy · scikit-learn (DBSCAN, HistGradientBoosting)
shapely STRtree point-in-polygon
rule engine + anomaly detector
Storage & API
SQLite (PostGIS-ready schema)
FastAPI — GeoJSON endpoints, background jobs
OpenAPI docs at /docs
Presentation
React 18 + Vite
Leaflet with canvas renderer (40 k+ points)
GeoJSON export → QGIS / ArcGIS / Google Earth
Design decisions
Around-cell Overpass queries + disk cache → OSM context scales India-wide
Canvas rendering, not DOM markers → smooth with tens of thousands of points
Offline demo archive + live mode share one code path → one env variable to go live
Everything is GeoJSON → plugs into any GIS NTRO already runs
Explainability first → analysts can audit, override, and feed corrections back
Notes: Keep this short unless asked. If a judge is technical: SQLite is deliberate for the hackathon; the schema and API are PostGIS-ready and we would add a tile server for multi-year national archives.

## Slide 12
DIFFERENTIATION
How this differs from what exists
ThermalSentinel · SIH26162 · NTRO
12
Capability | NASA FIRMS map | Generic fire dashboards | ThermalSentinel
Shows thermal anomalies on a map | ✔ | ✔ | ✔
Says what caused the anomaly (6 classes) | ✖ | ✖ | ✔
Separates industrial fire from wildfire / agri burning | ✖ | ◐ | ✔
Registry of persistent sources with history | ✖ | ✖ | ✔
Incident alert: FRP anomaly vs own baseline | ✖ | ✖ | ✔
Uses OSM infrastructure + land cover as context | ✖ | ✖ | ✔
Explains every decision (reasons) | ✖ | ✖ | ✔
Open GeoJSON API, GIS export | ◐ | ◐ | ✔
Free & open data only | ✔ | ◐ | ✔
Novelty: combining temporal persistence, OSM infrastructure context and physical signature in one explainable classifier, with baseline-relative anomaly alerts — none of the existing public tools do this.
Notes: If asked about published research: Liu et al. 2018 identified industrial heat sources from VIIRS Nightfire time-series; Elvidge et al. built global flare catalogues. We build on that idea but add OSM context, six-class discrimination, and operational alerting on a live GIS.

## Slide 13
WHY IT MATTERS
Impact & beneficiaries
ThermalSentinel · SIH26162 · NTRO
13
Disaster management
NDMA / SDMAs · fire services
Alerts only on abnormal industrial heat — 99 % fewer hotspots to triage
Faster, correctly-targeted response to plant fires and explosions
Standing watch on coal-seam fires (Jharia, Raniganj)
Security & strategic
NTRO and partner agencies
National registry of persistent thermal sources with activity history
Detect unregistered or undeclared industrial activity (persistent heat with no OSM facility)
Change detection: shutdowns, restarts, capacity surges
Environment & economy
CPCB · MoEFCC · insurers
Attribute district-level fires: stubble burning vs industry
Flaring inventories for emissions reporting
Verified incident records for insurance and compliance
Zero data cost · deployable on one VM or an air-gapped server · outputs plug into existing GIS · improves as analysts label real incidents.
Notes: Pick the beneficiary that matches the judge panel. For NTRO emphasise the middle column: a living registry of persistent heat sources — and the ability to spot activity where no facility is declared.

## Slide 14
ROADMAP
Where we take it next
ThermalSentinel · SIH26162 · NTRO
14
Done — prototype
End-to-end pipeline, 6-class hybrid classifier
Persistent-source registry + FRP-anomaly alerts
GIS dashboard, GeoJSON API, QGIS export
Offline labelled archive; live-FIRMS switch
Next round — validation
Live FIRMS ingestion for all India (MAP_KEY)
Validate against documented incidents (news / PESO / CPCB records)
Analyst feedback loop: label → retrain
Curated facility list to fill OSM gaps
Finals — scale & depth
Sentinel-2 SWIR chip classifier (CNN) per persistent source
ESA WorldCover 10 m raster where OSM is sparse
PostGIS + tile server, multi-year archive
Alerting: e-mail / SMS / webhook on anomalies
Our ask for the next round: access to any historical incident records NTRO / partner agencies can share, so we can validate against confirmed events.
Notes: Shows the judges we know what is missing. The honest limitation is validation on real, confirmed incidents — say it before they do, and turn it into an ask.

## Slide 15
ThermalSentinel
FIRMS tells you where it is hot.
We tell you what is burning — and whether it should be.
6
classes
114
persistent sources
138
incident alerts
99.9 %
accuracy
Live demo · http://localhost:5173 · API docs · http://127.0.0.1:8000/docs
Thank you — questions?
Notes: Close with the one-liner, then invite questions. Likely questions: clouds (answer: 90-day window + multiple passes; anomalies need persistence so one missed day does not matter), false alarms (answer: baseline-relative thresholds, explainable reasons, analyst override), scale (answer: around-cell OSM queries, PostGIS roadmap).